## Slide 1: Cargo securement standards 5291-PL-03.13

## Slide 2
Lesson goal
Resolving problems related to the load securing regulations.
Guide page 1
Notes: Référence : Guide des normes de charges et dimensions P.1

## Slide 3: GOAL
Ensure that cargo or objects transported by road vehicles are securely and properly fastened to maintain stability and prevent transported objects from falling or colliding with other vehicles.
Guide page 1
Notes: Référence : Guide des normes de charges et dimensions P.1

## Slide 4: Load securement standards regulation
It’s applies to:
Road vehicles with a GVWR of 4,500 kg or more or combinations of road vehicles with a GVWR of 4,500 kg or more.
Guide page 3
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 5: Definition of cargo securement tiedown
Load bar:
A device placed laterally between the walls of a vehicle to prevent tipping or shifting.
Guide page 4
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 6: Definition of cargo securement tiedown
Cradle:
Structure preventing a round article from rolling.
Guide page 4
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 7: Definition of cargo securement tiedown
Spacing block:
Any material placed under an item or between tiers to facilitate loading or unloading.
Guide page 5
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 8: Definition of cargo securement tiedown
Retaining wedge:
Wedge-shaped or tapered piece used to prevent round articles from rolling.
page 5
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 9: Definition of cargo securement tiedown
Front-end structure:
Vertical barrier behind a tractor cab capable of protecting the driver in case of forward cargo shift.
page 5
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 10: Definition of cargo securement tiedown
Edge protectors :
Device placed on the edge of cargo to prevent damage to a tiedown device or article.
page 5
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 11: Definition of cargo securement tiedown
Contained:
Cargo that is contained within a vehicle with walls and where each article is in contact with a wall and cannot move.
page 6
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 12: Tiedown definition
Specific element designed and manufactured to secure or tie down cargo such as a chain, strap, tensioner, etc.
page 6
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 13: Working load limit
Maximum load assigned by the manufacturer that can be applied to a component of a tie- down system or to a tiedown device under normal operating conditions
page 8
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 14: Working load limit (WLL)
page 8
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 15: Anchor point
A place that is part of the structure, fixtures, or accessories of a vehicle or cargo to which a tiedown device is attached.
page 8
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 16: Light vehicle
Automobile, light truck ou van with a net mass of 4500 kg or less.
page 12
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 17: Heavy duty vehicle
Vehicle with a net mass exceeding 4500 kg.
page 12
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 18: GENERAL REQUIREMENTS
page 12
Cargo inspection:
The driver of a vehicle carrying cargo must inspect the transported cargo and the securement system, and make appropriate adjustments:
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 19: GENERAL REQUIREMENTS
page 13
Before departure;
Within 80 km or less from the loading point;
After 240 km or 3 hours of driving;
At each change of activity;
Before leaving a private or public road.
Cargo inspection:
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 20: GENERAL REQUIREMENTS
page 13
Tiedown devices
All components of a cargo securement system must:
Be in proper working condition;
Be appropriate for their intended use;
Have no knots or damaged or weakened elements;
At each change of activity;
Before leaving a private or public road.
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 21: GENERAL REQUIREMENTS
page 13
Load securement devices
Securement devices, integrated locking devices, movable structures, and blocking devices must be fastened in such a way that they cannot unlock or loosen when the vehicle is traveling on a public road.
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 22: GENERAL REQUIREMENTS
page 14
Load securement devices
Securement devices, when possible, must be located within the rub rails if the vehicle is equipped with them.
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 23: GENERAL REQUIREMENTS Load securement system requirements
page 16
All cargo must be firmly immobilized or secured to prevent shifting, sliding, or tipping.
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 24: GENERAL REQUIREMENTS Cargo securement system working load limit
page 16
The sum of the Working Load Limits (WLL) of all securement devices used to secure an article or group of articles on a vehicle corresponds to the total WLL at 50%.
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 25: GENERAL REQUIREMENTS Cargo securement system working load limit
page 17
The WLL is identified by a marking
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 26: GENERAL REQUIREMENTS Cargo securement system working load limit
page 17
The WLL is identified by a marking
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 27: GENERAL REQUIREMENTS Tensioning of securement devices
page 19
A device must:
Be designed, constructed, and maintained so that the driver can tighten it.
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 28: GENERAL REQUIREMENTS Tensioning of cargo securing devices
page 19
A device must:
Be used un such a way that it cannot slip, tip over, come loose, open or detach when the vehicle is traveling on a public road.
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 29: Minimum number of tiedown devices Not blocked cargo
page 20
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 30: Minimum number of tiedown devices Not blocked cargo
page 20
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 31: Minimum number of tiedown devices Blocked cargo
page 21
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 32: EXERCISES Student notebook, competency 3
1.Give an example of a tiedown device
guide p.14
Load bar
Cradle
Retaining wedge
Edge protector
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 33: EXERCISES Student notebook, competency 3
2. Give an example of a tiedown device.
Chain;
Binder;
Stap.
guide p.14
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 34: EXERCISES Student notebook, competency 3
3.What means the letter WLL?
Working load limit: device capacity.
guide p.8
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 35: EXERCISES Student notebook, competency 3
4.What is the difference between a light vehicle and a heavy vehicle according to the regulations?
Light : less of 4500 kg GVWR,
Heavy : more of 4500 kg GVWR
guide p.12
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 36: EXERCISES Student notebook, competency 3
5. After loading a cargo, I drove 50 km and stopped for dinner. Am I required to inspect my cargo securement system?
Yes, because the cargo securement inspection must be performed at each change of duty status and before 80 km (50 miles).
guide p.13
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 37: MINIMUM NUMBER OF TIEDOWN DEVICES Based on the following illustrations, how many tiedown devices are needed for the following exercises?
DEVICES | LBS CAPACITY | KG CAPACITY
Strap | 5 400 lb | 2 450 kg
Chain | 6 600 lb | 2 990 kg
Binder | 5 400 lb | 2 450 kg
Anchor point | 5 500 lb | 2 500 kg
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 38: Student notebook, competency 3
Standard 10
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 39: Student notebook, competency 3
Standard 10
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 40: Securing cargo based on weight and lenght
Procedure: Apply the procedure based on weight and length, then choose the one that requires the highest number of securing devices.
Comp 3. student notebook
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 41: Secured based on weight and lenght
page 83
1.Cargo: wooden crate containing stained glass windows
Réponse:
4 700 kg ÷ 50 % = 2350 kg ÷ 2450 kg = 0.96 then 1 device
4 m ÷ 3.04 = 1.32 then 2 + 1 = 3 devices
3 devices
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 42: Load secure according to weight and length
page 83 guide
2. Cargo: steel beams.
Réponse:
10 000 kg ÷ 50 % = 5000 kg ÷ 2450 kg = 2.04 then 3
6.2 m ÷ 3.04 = 2.03 then 3 + 1 = 4 devices
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 43: Load secure according to weight and length
page 83 guide
3. Cargo: aluminium and wood structures for construction
Réponse:
8 000 kg ÷ 50 % = 4 000 kg ÷ 2450 kg = 1.63 then 2 8.9 m ÷ 3.04 = 2.93 then 3 + 1 = 4
12 000 kg ÷ 50 % = 6 000 kg ÷ 2450 kg = 2.45 then 3 5.9 m ÷ 3.04 = 1.94 then 2 + 0 = 2
7 devices
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 44: Load secure according to weight and length
page 84
4. Cargo: Metal pipes in wooden crates
Réponse:
18 000 kg ÷ 50 % = 9 000 kg ÷ 2450 kg = 3.67 then 4 6.05 m ÷ 3.04 = 1.99 then 2 + 1 = 3
12 000 kg ÷ 50 % = 6 000 kg ÷ 2450 kg = 2.45 then 3 7.9 m ÷ 3.04 = 2.60 then 3 + 0 = 3
7 devices
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 45: Load secure according to weight and length
page 84
5. Cargo: Copper block for machining
Réponse:
11 000 kg ÷ 50 % = 5 500 kg ÷ 2450 kg = 2.24 then 3
2 m ÷ 3.04 = 0.66 then 1 + 0 = 1
3 devices
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 46: Load secure according to weight and length
page 84 guide
6. Cargo: aluminium block for machining
Réponse:
1 200 kg ÷ 50 % = 600 kg ÷ 2450 kg = 0.24 then 1
1.52 m ÷ 3.04 = 0.5 then 1 + 1 = 2
2 devices
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 47: MINIMUM NUMBER OF CARGO DEVICE For the following exercises, consult the table below to know the capacity of lashing equipment and anchor points?
page 85 guide
DEVICES | LBS CAPACITY | KG CAPACITY
Strap | 5 400 lb | 2 450 kg
Chain | 6 600 lb | 2 990 kg
Binder | 5 400 lb | 2 450 kg
Anchor point | 5 500 lb | 2 500 kg
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 48: Load secure according to weight and length
page 85 guide
7. Cargo: Crates containing parts from the port.
Réponse:
8 000 kg ÷ 50 % = 4 000 kg ÷ 2248 kg = 1.78 then 2 4,0 m ÷ 3.04 = 1,31 then 2+1=3
7 300 kg ÷ 50 % = 3 650 kg ÷ 2248 kg = 1.62 then 2 4,0 m ÷ 3.04 = 1,31 then 2
5 devices
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 49: Load secure according to weight and length
page 85 guide
8. Cargo: Concrete barriers
Réponse:
16 800 kg ÷ 50 % = 8 400 kg ÷ 2248 kg = 3.74 then 4
6,5 m ÷ 3.04 = 2,13 then 3 + 1 = 4
4 devices
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 50: Load secure according to weight and length
page 86 guide
9. Cargo: Military tool boxes from northern Quebec
Réponse:
13 500 kg ÷ 50 % = 6 750 kg ÷ 2248 kg = 3.003 then 4 6 m ÷ 3.04 = 1.97 then 2 + 1 = 3
1 000 kg ÷ 50 % = 500 kg ÷ 2248 kg = 0.22 then 1 4,0 m ÷ 3.04 = 1,97 =2
6 devices
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 51: Load secure according to weight and length
page 86 guide
10. Cargo: Dunnage tool box
Réponse:
490 kg ÷ 50 % = 245 kg ÷ 2248 kg = 0,10 then 1 and - of 500 kg
1,5 m ÷ 3.04 = 0,49 = 1 because - of 1,52m
1 device
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 52: Load secure according to weight and length
page 86 guide
11. Cargaison: Dunnage tool box
Réponse:
510 kg ÷ 50 % = 255 kg ÷ 2248 kg = 0,11 then 1+1=2 because more of 500 kg
1,5 m ÷ 3.04 = 0,49 = 1 + 1 then 2
2 devices
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 53: Load secure according to weight and length
page 87 guide
12. Cargo: Block granite
13 500 kg ÷ 50 % = 6 750 kg ÷ 2248 kg = 3.002 then 4 4,0 m ÷ 3.04 = 1,31 = 2 + 1 = 3
8 500 kg ÷ 50 % = 4 250 kg ÷ 2248 kg = 1.89 then 2 4,0 m ÷ 3.04 = 1,31 = 2
9 000 kg ÷ 50 % = 4 500 kg ÷ 2248 kg = 2.001 then 3 3,0 m ÷ 3.04 = 0.98 + 1 = 2
9 000 kg ÷ 50 % = 4 500 kg ÷ 2248 kg = 2.001 then 3 3,0 m ÷ 3.04 = 0.98 = 1
12 devices
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 54: Load secure according to weight and length
page 87 guide
13. Cargo: Concrete bases and steel dock sections
12 000 kg ÷ 50 % = 6 000 kg ÷ 2248 kg = 2.66 then 3 3 m ÷ 3.04 = 0,98 then 1
12 000 kg ÷ 50 % = 6 000 kg ÷ 2248 kg = 2.66 then 3 3 m ÷ 3.04 = 0,98 then 1
7 300 kg ÷ 50 % = 3 650 kg ÷ 2248 kg = 1.62 then 2 6,08 m ÷ 3.04 = 2 then 2 + 1 = 3
5 100 kg ÷ 50 % = 2 550 kg ÷ 2248 kg = 1.13 then 2 3.04 m ÷ 3.04 = 1
11 devices
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 55: Load secure according to weight and length
page 87 guide
14. Cargo: Bundles of slate roofing shingles
4 000 kg ÷ 50 % = 2 000 kg ÷ 2248 kg = 0.88 then 1 2,0 m ÷ 3.04 = 0.65 then 1
7 000 kg ÷ 50 % = 3 500 kg ÷ 2248 kg = 1.55 then 2 2,0 m ÷ 3.04 = 0.65 then 1 +1 = 2
8 000 kg÷ 50 % = 4 000 kg ÷ 2248 kg = 1.77 then 2 2,0 m ÷ 3.04 = 0.65 then 1
9 000 kg ÷ 50 % = 4 500 kg ÷ 2248 kg = 2.001 then 3 2,0 m ÷ 3.04 = 0.65 then 1
4 450 kg ÷ 50 % = 2 225 kg ÷ 2248 kg = 0.98 then 1 2,0 m ÷ 3.04 = 0.65 then 1
9 devices
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 56: Load secure according to weight and length
page 88 guide
15. Cargo: Steel beams
Réponse:
12 000 kg ÷ 50 % = 6 000 kg ÷ 2248 kg = 2,66 then 3
14,9 m ÷ 3.04 = 4.90 then 5 + 1 = 6
6 devices
Notes: Référence : Guide des normes de charges et dimensions P.2 (Empattement)

## Slide 57
Thank you for your attention