## Slide 1: Class 1 Learner training program
Commission scolaire de la Rivière-du-Nord
CHAPTER 6
COPING WITH DANGEROUS
SITUATIONS

## Slide 2: WHAT TO DO IN CASE OF A TIRE PUNCTURE
Conduire un véhicule lourd 163
Puncture of a Rear Tire on a Dual-Wheeled Vehicle
The puncture of one of the tires on a dual-wheeled semi-trailer has little effect on driving. The vehicle still maintains its stability. However, the additional load that the other tire must bear can damage it. Additionally, if one of the rear tires of the tractor blows out, a vibration may occur at the back of the tractor.
Often, the best way to determine if a tire has suffered a puncture, aside from noise or vibration, is to stop your vehicle and check the condition of the tires yourself. If one of the tires is flat, you must cease driving the vehicle until it is repaired or replaced.
Puncture of a Front Tire or a Rear Tire on a Non-Dual-Wheeled Vehicle
The puncture of a front tire or a rear tire on a non-dual-wheeled vehicle often results in a loss of control of the vehicle.
To maintain control of your vehicle, it is advisable to:
Hold the steering wheel firmly to maneuver off the roadway.
Gradually release the accelerator and
Slowly apply the brakes to bring the vehicle to a stop in a safe location.

## Slide 3: WHAT IS HYDROPLANING AND HOW SHOULD YOU REACT?​
Conduire un véhicule lourd 165
Rydroplaning occurs when vehicle tires lose traction, particularly when puddles form on the road surface due to rain. A thinlayer of water then forms between the tire and the road surface, causing the tires to lose their grip on the road. Hydroplaning can be even worse if your tires are underinflated or the tread is worn.​
What should you do?​
To maintain control of your vehicle: you shall :​
​Take your foot off the accelerator.​
​Avoid braking, since this could cause you to lose control of your vehicle. Once you have regained control of your vehicle, resume normal speed.​

## Slide 4: ​WHAT CAUSES SKIDDING?​
Conduire un véhicule lourd 166
Most of the time, skidding is caused by travelling too fast on damaged, slippery or snow-covered road surfaces. When this happens, the tires lose their traction and tend to skid. This can happen if you brake too abruptly, if you take a curve too quickly, or if you are driving up or down a hill.​
Braking abruptly​
Driving up or down a hill​

## Slide 5: How to avoid skidding​
Conduire un véhicule lourd 167
It is very hard to regain control of a heavy vehicle once it goes into a skid. The best approach is to drive defensively and try to avoid skidding.​
Ways to avoid skidding​
​Reduce your speed as dictated by road conditions and layout.​
Maintain a sufficient distance between your vehicle and other road users, especially when the pavement is slippery. This will help you avoid having to brake abruptly, which is one of the most frequent causes of skidding.​
​Check your semi-trailer in the rearview mirrors every time you brake. Let up on your brakes if the semi-trailer is starting to skid.​
Do not use the hand brake to slow down your vehicle.​
​
​​
​

## Slide 6: HOW TO RECOVER FROM A SKID
In situations where defensive driving is not enough to avoid skidding, the first thing to do is determine the cause of the skid.​
If the skid is caused by overbraking:​
​Let go on the brake pedal so that your wheels start turning again and the tires can grip the pavement.​
​
If the skid is caused by rapid downshifting:​
​Press down on the clutch.​
​IMPORTANT : Use the brake pedal as needed. Once you have recovered control of your vehicle, shift into the appropriate gear.​
Conduire un véhicule lourd 168

## Slide 7: If the skid is caused by over accelerating:​
Conduire un véhicule lourd 168
Slowly release the accelerator in order to regain control of your vehicle.​
​
IMPORTANT: Change gears as needed to keep your wheels from spinning, while bearing in mind the effects of compression by the engine and the supplemental brakes.​

## Slide 8: Maintain steering control​
If the rear end of the vehicle is skidding to the right:​
If the rear end of the vehicle is skidding to the left:
1. Turn the steering wheel to the left to pull the vehicle back into a straight line.​
2. When the vehicle is almost back in line, turn the steering wheel to the right until the front wheels are lined up straight.​
Whether a skid is caused by braking abruptly, accelerating quickly or a loss of traction in a curve, the rear end of the vehicle will veer to the left or to the right. To stop your vehicle from skidding completely out of control, you must turn your steering wheel in the same direction your vehicle is skidding.​
Conduire un véhicule lourd 169
Turn the steering wheel to the right to pull the vehicle back into a straight line.​
When the vehicle is almost back in line, turn the steering wheel to the left until the front wheels are lined up straight.​

## Slide 9: WHAT CAUSES JACKKNIFING?​
Conduire un véhicule lourd 170
Jackknifing is caused when the forward thrust of the semi-trailer pushes the tractor over to the left or to the right. The tractor and semi-trailer are said to have jackknifed if they wind up positioned at an angle of less than 90°.​
If you notice that you are losing traction, you must quickly let up on the accelerator or the brake pedal, as applicable, to avoid jackknifing.​

## Slide 10: HOW TO MAKE AN EMERGENCY STOP​
Conduire un véhicule lourd 171
Today, most heavy vehicles are equipped with an anti-lock brake system (ABS) that prevents the wheels from locking if the brakes are applied abruptly. However, circumstances may require you to drive a vehicle not equipped with an ABS system. If so, you must be able to use the proper technique to make an emergency stop without causing the wheels to lock up, as explained below:​
Press down on the brake pedal ​
Gradually increase pressure on the brake pedal, as far as you can without causing your wheels to lock up, until you bring your vehicle to a complete stop.​
​If you see that your wheels are locking up, let go of the brake pedal 6 slightly to keep from losing control of your vehicle. Resume pressure on the brake as soon as the wheels start turning again, making sure that the wheels do not lock up.​

## Slide 11: IF YOUR BRAKES SHOULD FAIL WHILE DRIVING DOWN A HILL​
Conduire un véhicule lourd 174
Brakes are designed to withstand a certain amount of heat, but if you apply them too often or for too long at a time, they can overheat. Before starting down a steep grade, make sure that your brakes are in good condition. If you are not sure, pull over and check them.​
​If, despite all of these precautions, you realize that your brakes are not working properly, you will have to find a way of slowing down and stopping your vehicle quickly without losing control of it. Time is of the essence here because the greater your speed, the harder it will be to stop your vehicle.​

## Slide 12: If there is no emergency stopping area
Conduire un véhicule lourd 175
You must steer your vehicle to a safe location to stop. It is important to locate a place where the vehicle can be safely immobilized as quickly as possible.
If there is an emergency stopping area:
You can use it; this will allow for a complete and safe stop. You can know the presence of such a roadway feature even before you enter the incline. In fact, the STOPPING AREA sign, accompanied by a distance indication, indicates the presence of an emergency lane with a stopping area, allowing for the safe immobilization of a vehicle whose braking system has become ineffective. This is followed by the S.O.S. STEEP SLOPE sign, which indicates the approach of a particularly steep slope that includes an emergency lane. By following the indications accompanying the successive STOPPING AREA signs, you will be able to take the emergency lane that leads to it.