## Slide 1: Class 1 learner training program
CHAPTER 7 ​
TRANSPORTATION OF PASSENGERS​
Commission scolaire de la Rivière-du-Nord

## Slide 2: LAWS AND REGULATIONS
Conduire un véhicule lourd 181
Drivers who carry passengers must be familiar with the applicable laws and regulations to perform their work properly. The principal bodies responsible for enforcing these laws and regulations are the Société de l’assurance automobile du Québec, the Ministère des Transports, de la Mobilité durable et de l’Électrification des transports du Québec and the Commission des transports du Québec.​
​In addition to the Highway Safety Code, which applies to all drivers, professional drivers carrying passengers are subject to other laws and regulations governing this form of transportation, including the following:​
​
Transport Act​
Bus Transport Regulation​
​Regulation respecting road vehicles used for the transportation of school children​
​Regulation respecting the hours of driving and rest of heavy vehicle drivers​
Regulation respecting safety standards for road vehicles​

## Slide 3: ​NUMBER OF PASSENGERS​
For buses used to carry school children
Conduire un véhicule lourd 182
The number of passengers allowed corresponds to the number of seating positions​
​When driving a school bus, you may not allow more than three school children on one seat.​
​There must be sufficient space for each child so that he or she can be seated safely and without blocking the aisle.​
For buses not used to carry school children​
For buses travelling outside an urban area (such as chartered), the maximum number of passengers allowed corresponds to the number of seating positions, plus one place for a standing passenger for each row of seats. ​
​
For buses travelling in an urban area (such as mass transit buses), ​
the Code sets no limit on the number of passengers allowed on board.​

## Slide 4: RULES FOR THE ROAD​
Conduire un véhicule lourd 183
Picking up and dropping off passengers​
Before picking up or dropping off passengers, you must pull over and come to a full stop on the far right-hand side of the road or in a special area designated for that purpose.. ​
​Once you have stopped, you may not open your door until you have made sure that it is safe to do so.​

## Slide 5: While driving​
There are various traffic rules bus drivers must obey to protect the safety of their passengers and other road users. For example:​
You may not drive on after stopping if anyone is leaning against the outside of the bus (the bumper, for example);​
​Before driving on, you must make sure that none of the passengers you have just dropped off is at risk of being struck by the bus or getting caught underneath it.​
​On roads within city limits where the posted speed limit is under 70 km/h, a bus has the right of way when pulling back into the lane it was using before it stopped. Nevertheless, you must use good judgment at all times and make sure you can pull back into your lane without endangering other road users. This means that before pulling away from the curb, you must make sure the way is clear and click on your turn signal lights.
Conduire un véhicule lourd 184

## Slide 6: While driving (next)​
At level crossings, you must slow down and make sure you can stop without endangering other road users. You must stop your vehicle at least 5 m from the crossing, and you may not proceed until there is enough room between you and any vehicle ahead of your bus for you to clear the crossing completely, regardless of any traffic lights. You are exempted from this obligation only if there is an EXEMPT sign posted.;​
Even though buses are subject to mechanical inspection rules, you do not have to stop at inspection stations, unless the bus is hauling a trailer.;​
Conduire un véhicule lourd 185

## Slide 7: While driving (next)​
Even though buses are subject to mechanical inspection rules, you do not have to stop at inspection stations, unless the bus is hauling a trailer;​
​
When driving any vehicle with a total loaded mass of 3,000 kg or more, including a bus, you must pull over when you come to a brake check area designated by a VÉRIFICATION sign.​
You must come to a full stop at the stop sign and check the brakes yourself. As a complementary measure, we recommend that you also follow the brake inspection procedure outlined in Chapter 12.​
Conduire un véhicule lourd 185

## Slide 8: SCHOOL BUSES​
Conduire un véhicule lourd 186
Driver training​
A special school bus driver training course has been developed to meet this need. School bus and minibus drivers are required to have a certificate of competency issued by one of the two existing road transport training centres, in addition to a driver’s licence of the appropriate class.​
​To obtain this certificate, drivers have to pass a 15-hour training course (Basic training program for school bus drivers) dealing with the role and responsibilities of school bus drivers, rules relating to safety equipment, techniques for picking up and dropping off school children, and emergency response. They must also renew their certificate every 3 years after completing 6 hours of supplementary training.​
​Experienced drivers must be able to adjust to unforeseen circumstances. They must show tact and initiative in settling disputes and dealing with unruly youngsters. They also need to know something about the behaviour of the school children they carry.​

## Slide 9: SCHOOL BUS (next)​
Conduire un véhicule lourd 187
Picking up and dropping off school children​
When picking up or dropping off children, school bus drivers must first slow down and move over to the right side of the lane or, where applicable, the parking area.​
​Then (unless you are driving a vehicle that carries wheelchair passengers exclusively), there are two phases involved in bringing the bus to a stop:​
Switch on the alternately flashing yellow warning lights to alert other motorists or cyclists that the bus is about to stop. (School buses built before August 29, 2005 are not equipped with alternately flashing yellow warning lights and are exempt from this requirement, but the hazard lights must be switched on).​
​Switch on the flashing red lights and activate the mandatory stop sign. You may not pick up or drop off school children unless the flashing red lights are switched on.​

## Slide 10: SCHOOL BUS (next)​
Conduire un véhicule lourd 188
Picking up and dropping off school children (next)​
You must also switch on your flashing lights and stop sign if you are parked behind another school bus whose flashing lights are on, even if you are not dropping off or picking up schoolchildren.​
​You may not use your flashing lights or stop sign in any other circumstances.​
​
While driving​
You may not drive on after stopping until you are sure that all of your passengers are seated and the bus door is closed. In addition, you may never leave your school bus if there are passengers still on board unless absolutely necessary.​

## Slide 11: SCHOOL BUS (next)​
Conduire un véhicule lourd 188
Mandatory equipment​
You are responsible for making sure that your school bus is equipped with the following:​
​three reflective warning triangles; ​
one dry-chemical fire extinguisher installed inside the bus near the front door and properly secured in a box within reach of the driver;​
​one complete first-aid kit solidly installed within reach of the driver. The contents of the kit are prescribed by regulation.​

## Slide 12: SECURING BAGGAGE​
It is prohibited to carry any item weighing over 50 kg and having a volume of more than 0.450 m3 inside a motor coach.​
​The passengers’ baggage must be distributed and secured in such a way that it cannot move around freely during the trip. If baggage comes loose, it may cause injury to passengers or distract the driver.​
​Motor coach drivers who carry packages and baggage in addition to passengers must stow these items in the compartments designed for that purpose.​
Conduire un véhicule lourd 189